## Slide 1: Hardware

## Slide 2
https://www.youtube.com/watch?v=mzy84Vb_Gxk

## Slide 3: The Microcontroller Spectrum
Application Specific
Prototype
General Purpose
Atmega328
Requires approx. 10% of Arduino hardware to function
Arduino compatible programming
Arduino
Atmega328
All support hardware included
  USB programming
  Power regulation
  Pins “Broken out”
C-like programming language
Tessel
RISC based
Includes WIFI and Ethernet
Javascript based (NodeJS)
Pins “Broken out”
Raspbery Pi
A fully functioning computer(!)
Pins “broken out”

## Slide 4: Arduino
“The immediate precursor to the Arduino was a custom-made Wiring microcontroller created by the artist/ designer Hernando Barragan in 2004 for his masters thesis (at Institute Design Institute Ivrea), intended for use by a “non-technical audience” of “artists, designers, and architects”
“The Arduino incorporated the following characteristics: a programming environment based on Processing language (a programming language conceived by Ben Fry and Casey Reas, also conceived for artists/ designers), the ability to program the board via a standard USB connection, and a low price point (starting at about $35 USD)”
http://www.kenleung.ca/portfolio/arduino-a-brief-history-3/

## Slide 5: Arduino
Arduino is
  A bootloader
  An IDE
  A programming language (But it’s basically “just” C)
  A device
Development environment is free
Thousands of libraries
Started as “Wiring” and “Processing”
  What existed before?
  Atmel studio
  Now “free”, previously expensive
  There is still a paid for version
    Price is a mystery, purchasing is a mystery “Contact them”

## Slide 6
Arduino UNO |  | 
Flash memory | 32 KB | Storage for code
RAM | 2 KB | Storage for variables
EEPROM | 1 KB | Long term storage
Clock speed | 16 Mhz | Equivalent to a 1980’s CPU
Power consumption | 0.29 W | 
Weight | 25 g | 
Apollo Guidance Computer (1966) |  | 
Flash memory | 0 KB | 
RAM | 4 KB | Storage for variables
EEPROM | 74 KB | Storage for code
Clock speed | 2 Mhz | 
Power consumption | 55 W | 
Weight | 32 Kg | 

## Slide 7: What is an Arduino for?
Analog Input/Output pins read and write any voltage in the range 0V to 5V. Uses:
Reading sensors
Setting servo motors
Digital Input/Output read and write Low or High signals.
Low = 0V = GND
High = 5V
Uses:
Writing to displays
Serial input/output
Power and programming over USB
Arduino’s, or microcontrollers in general, are a platform for prototyping electronics. They allow you to read from sensors, control actuators and screens, and communicate with computers, all through code.
Most projects require very little knowledge of electronics.

## Slide 8
2001: Processing Programming Language
2004: Wiring
2005: Arduino
2014: ESP8266
$2 Wifi microcontroller(!)

## Slide 9: Tessel
Tessel is:
  A device
  A software framework
Tessel runs NodeJS – Javascript
  Any package on NPM runs on tessel
Launched by a Boston based startup in 2013

## Slide 10
Tessel 2 |  | 
Flash memory | 32 MB | Storage for code
RAM | 64 MB | Storage for variables
EEPROM | 1 KB | Long term storage
Clock speed | 580 Mhz | 
Power consumption | 0.85 W | 
Weight | 68 g | 
Atmel coprocessor | 48 Mhz | Realtime microcontroller
Apollo Guidance Computer (1966) |  | 
Flash memory | 0 KB | 
RAM | 4 KB | Storage for variables
EEPROM | 74 KB | Storage for code
Clock speed | 2 Mhz | 
Power consumption | 55 W | 
Weight | 32 Kg | 

## Slide 11: Tessel
WiFi Antenna
IO Pins – See next slide
MicroUSB and Regular USB for power and/or programming
Ethernet for network, can also provide power
Tessel can be programmed over USB, Ethernet, or WiFi!

## Slide 12: Tessel Pin Map
SCL/SDA/SCK; MISO/MOSI; Tx/Rx: Serial communication, allowing microcontrollers to talk directly to each other, or to a computer.
Interrupt: If this pin is set (externally) to high, it will trigger an interrupt callback in the microcontroller, which will run instead of the already running code
PWM: Pulse Width Modulation, allows you to write a value 0-255 to a pin

## Slide 13: Why Tessel?
WiFi + Javascript

## Slide 14: Example: LEDs
The Battery provides current at fixed voltage
The resistor provides resistance which changes the current (V=IR)
The brightness of the LED is determined by how much current is supplied

## Slide 15: Example: LEDs
In the initial example, the battery simply provides a constant voltage, driving a current in the circuit. If the battery is flat, the voltage (or Potential) at + and - is 0V, so no current flows. For current flow the potential at + must by higher than at –.
We can exploit this to switch an LED on/off using pins on a microcontroller.

## Slide 16: Example: LEDs
Pins, marked here as 0, 1, 2, etc, can be set in code to be high or low.
High = potential of 3.3V
Low = potential of 0V
GND in this case is a potential of 0V

## Slide 17: Arduino

## Slide 18: Arduino

## Slide 19: Tessel Setup
Open a terminal and run
  npm install –g t2-cli
Check it’s working
  t2 list
Name your tessel
  t2 rename <name>
Connect to WiFi
  T2 wifi –n “MIT”
  If MIT doesn’t work, try “MIT GUEST”

## Slide 20: Blink on Tessel

## Slide 21: Blink on Tessel
t2 run index.js

## Slide 22: Components
Ambient
LED Matrix
Light sensor
Sound sensor
Designed and manufactured by for Tessel
LED Matrix
Support Hardware
  Serial interface
  Control 64 LED’s with only 4 wires

## Slide 23: Tessel Modules - Full List (https://tessel.io/modules)

## Slide 24: Case Study: The Blue Button
1 Button. 1 Electric Imp
Uses: Various

## Slide 25: Case Study: Cards Against Humanity Printer
Electric Imp for WiFi
Thermal Printer – Receipt printer
Prints random cards from reddit
NOT SAFE FOR WORK
Reddit.com/r/cahideas

## Slide 26: Case Study: Toolpass
System to manage access to our laser cutter
Users log in using their Charlie Card
Logs member usage for billing
Reports activity on slack
Slack Messages
Server
Toolpass
Laser Cutter
Switch on/off
Laser Fired
Charlie Card,
Laser usage
User auth

## Slide 27: Case Study: Toolpass

## Slide 28: Hardware examples
https://www.ted.com/talks/neil_harbisson_i_listen_to_color
http://www.bbc.com/news/technology-37775605

## Slide 29: Tessel Ambient Module
{
"name": "hello",
"version": "0.0.0",
"description": "Tessel project",
"main": "index.js",
"dependencies" :
{
"ambient-attx4" : "0.2.11",
"mqtt" : "2.0.1",
"backpack-ht16k33" : "0.2.1"
}
}
package.json
var tessel = require('tessel');
var ambientlib = require('ambient-attx4');
var ambient = ambientlib.use(tessel.port['A']);
ambient.on('ready', function () {
// Get points of light and sound data.
setInterval( function () {
ambient.getLightLevel( function(err, lightdata) {
if (err) throw err;
ambient.getSoundLevel( function(err, sounddata) {
if (err) throw err;
console.log("Light level:", lightdata.toFixed(8), " ", "Sound Level:", sounddata.toFixed(8));
});
});
}, 500); // The readings will happen every .5 seconds
});
index.js

## Slide 30: Send a tweet!
{
"name": "hello",
"version": "0.0.0",
"description": "Tessel project",
"main": "index.js",
"dependencies" :
{
"ambient-attx4" : "0.2.11",
"mqtt" : "2.0.1",
"backpack-ht16k33" : "0.2.1“,
“twitter" : “1.4.0"
}
}
package.json
var twitter = require('twitter');
// authentication for https://twitter.com/course1_125
var twit = new twitter({
consumer_key: 'sCPDZyS0yJRMrdOZ8T2vXFC1R',
consumer_secret: 'VYe5JX7G0nVWsG4wouyONviHYIdPLZJ79w1wFIv8jhUdEAdBaK',
access_token_key: '783748853409406976-1mrcIng9HwtyAxRaxaUnPHjlRoYuWQ6',
access_token_secret: 'lIuWaXEZRc4xY9GgPhkrtYPCcvKhIJz1YDwmtMKiY82hr'
});
twit.post('statuses/update', {status: “Your message here!”}, function(error, tweet, response) {
index.js

## Slide 31: Connecting the LED Matrix
LED Matrix | SCL | SDA | GND | VCC
Tessel | A/B 0 | A/B 1 | GND | 3V3
Which pins to connect

## Slide 32: Tessel LED Matrix
{
"name": "hello",
"version": "0.0.0",
"description": "Tessel project",
"main": "index.js",
"dependencies" :
{
"ambient-attx4" : "0.2.11",
"mqtt" : "2.0.1",
"backpack-ht16k33" : "0.2.1"
}
}
package.json
var tessel = require("tessel");
var backpack = require('backpack-ht16k33').use(tessel.port['B']);
backpack.on('ready', function() {
backpack.clear();
setInterval(function() {},500); // Keep the tessel alive
//backpack.writeBitmap(smile);
backpack.animate(frames,500);
//backpack.scroll(smile,500);
});
var frames = [smile, straight, frown];
// Add bitmaps from next slide
Index.js

## Slide 33: Tessel LED Matrix
var smile = [
[0,0,1,1,1,1,0,0],
[0,1,0,0,0,0,1,0],
[1,0,1,0,0,1,0,1],
[1,0,0,0,0,0,0,1],
[1,0,1,0,0,1,0,1],
[1,0,0,1,1,0,0,1],
[0,1,0,0,0,0,1,0],
[0,0,1,1,1,1,0,0],
];
var straight = [
[0,0,1,1,1,1,0,0],
[0,1,0,0,0,0,1,0],
[1,0,1,0,0,1,0,1],
[1,0,0,0,0,0,0,1],
[1,0,0,0,0,0,0,1],
[1,0,1,1,1,1,0,1],
[0,1,0,0,0,0,1,0],
[0,0,1,1,1,1,0,0],
];
var frown = [
[0,0,1,1,1,1,0,0],
[0,1,0,0,0,0,1,0],
[1,0,1,0,0,1,0,1],
[1,0,0,0,0,0,0,1],
[1,0,0,1,1,0,0,1],
[1,0,1,0,0,1,0,1],
[0,1,0,0,0,0,1,0],
[0,0,1,1,1,1,0,0],
];