## Slide 1: Internet of Things

## Slide 2: The Microcontroller Spectrum
Application Specific
Prototype
General Purpose
Atmega328
Requires approx. 10% of Arduino hardware to function
Arduino compatible programming
Arduino
Atmega328
All support hardware included
  USB programming
  Power regulation
  Pins “Broken out”
C-like programming language
Tessel
RISC based
Includes WIFI and Ethernet
Javascript based (NodeJS)
Pins “Broken out”
Raspbery Pi
A fully functioning computer(!)
Pins “broken out”

## Slide 3: Tessel runs Javascript
WiFi Antenna
IO Pins
MicroUSB and Regular USB for power and/or programming
Ethernet for network, can also provide power

## Slide 4: Why Tessel?
WiFi + Javascript

## Slide 5: Example: LEDs
The Battery provides current at fixed voltage
The resistor provides resistance which changes the current (V=IR)
The brightness of the LED is determined by how much current is supplied

## Slide 6: Example: LEDs
In the initial example, the battery simply provides a constant voltage, driving a current in the circuit. If the battery is flat, the voltage (or Potential) at + and - is 0V, so no current flows. For current flow the potential at + must by higher than at –.
We can exploit this to switch an LED on/off using pins on a microcontroller.

## Slide 7: Example: LEDs
Pins, marked here as 0, 1, 2, etc, can be set in code to be high or low.
High = potential of 3.3V
Low = potential of 0V
GND in this case is a potential of 0V

## Slide 8: Blink on Tessel

## Slide 9: Tessel Modules - Full List (https://tessel.io/modules)

## Slide 10: Hardware examples
https://www.ted.com/talks/neil_harbisson_i_listen_to_color
http://www.bbc.com/news/technology-37775605

## Slide 11: Case Study: The Blue Button
1 Button. 1 Electric Imp
Uses: Various

## Slide 12: Case Study: Cards Against Humanity Printer
Electric Imp for WiFi
Thermal Printer – Receipt printer
Prints random cards from reddit
NOT SAFE FOR WORK
Reddit.com/r/cahideas

## Slide 13: Case Study: Toolpass
System to manage access to our laser cutter
Users log in using their Charlie Card
Logs member usage for billing
Reports activity on slack
Slack Messages
Server
Toolpass
Laser Cutter
Switch on/off
Laser Fired
Charlie Card,
Laser usage
User auth

## Slide 14: How do devices communicate?

## Slide 15: Serial Communication
Send data bit by bit
Format and transfer rate must be agreed at both ends

## Slide 16: HTTP

## Slide 17: HTTP: RESTful
A “request” is sent to a server via URL
  Eg. http://api.example.com/resources/user/1036721?name=something
Response is usually text in HTML, XML, or JSON
Great if your asking for something
  What about “push”
  Eg. Server wants to tell device to do something
Path or variables
variables

## Slide 18: HTTP: RESTful Hypothetical Light Switch
Server
Cell Phone
api.example.com/turnoff
WiFi Switch
Should I turn off?
Process Response
Turn off
No
Yes
api.example.com/shoulditurnoff

## Slide 19: MQTT: Message Queuing Telemetry Transport

## Slide 20: MQTT
MQTT was invented by Andy Stanford-Clark (IBM) and Arlen Nipper (Arcom, now Cirrus Link) back in 1999, where their use case was to create a protocol for minimal battery loss and minimal bandwidth connecting oil pipelines over satellite connection. They specified the following goals, which the future protocol should have:
  Simple to implement
  Provide a Quality of Service Data Delivery
  Lightweight and Bandwidth Efficient
  Data Agnostic
  Continuous Session Awareness

## Slide 21: MQTT: Pub/Sub
Clients connect to a “Broker”
Clients subscribe to topics eg,
  client.subscribe(‘toggleLight/1’)
  client.subscribe(‘toggleLight/2’)
  client.subscribe(‘toggleLight/3’)
Clients can publish messages to topics:
  client.publish(‘toggleLight/1’, ‘toggle’);
  client.publish(‘toggleLight/2’, ‘toggle’);
All clients receive all messages published to topics they subscribe to
Messages can be anything
  Text
  Images
  etc

## Slide 22: MQTT Hypothetical Light Switch
Broker
Cell Phone
client.publish(‘lightSwitch/1’, ‘toggle’)
WiFi Switch
Toggle Switch
‘toggle’

## Slide 23: Websockets
Chrome supports HTTP, HTTPS, FILE, FTP, WS (websockets).
Chrome does not support MQTT
But you can do MQTT over websockets!
What is websockets?

## Slide 24: Websockets

## Slide 25: Websockets
var webSocketServer = require('ws').Server;
var wss = new webSocketServer({port: 8080});
// broadcast client message to all
wss.broadcast = function broadcast(data) {
wss.clients.forEach(function each(client) {
client.send(data);
});
};
// catch client messages
wss.on('connection', function connection(ws) {
ws.on('message', function incoming(message) {
console.log('received from %s', message);
wss.broadcast(message);
});
});
var webSocketClient = require('ws');
var ws = new webSocketClient('ws://localhost:8080');
var id = Math.floor(Math.random()*10000);
ws.on('message', function(message) {
console.log('received from %s', message);
});
function sendMessage(){
var timeStamp = Date.now();
var message = 'clientId:' + id + ', '
+ 'timeStamp:' + timeStamp;
ws.send(message);
}
function timer(){
sendMessage();
setTimeout(timer, 3000);
}
ws.on('open', function() {
timer();
});
server.js
client.js

## Slide 26: MQTT Over Websockets
We can still use MQTT in a browser
The connection is handled via Websockets
This eliminates a lot of the “housekeeping” required by Websockets
Many to many communication much easier

## Slide 27: MQTT
client = mqtt.connect('ws://162.243.219.88', { port: 9001 });
client.on('connect', function () {
console.log('Connected to MQTT broker!’);
client.subscribe('TestChannel’);
client.publish('TestChannel', "Hello Test Channel!");
});
client.on('message', function (topic, message) {
console.log(topic);
console.log(message.toString());
});

## Slide 28: MQTT in the wild

## Slide 29: The Broker
IP Address: 162.243.219.88
MQTT Port: 1883 (For running in NodeJS)
Websocket Port: 9001 (For running in a web browser)
Broker is running on DigitalOcean
  https://www.digitalocean.com/
Broker is Mosquitto
  https://mosquitto.org/

## Slide 30: Channels in MQTT
Channels/topics in MQTT work like file paths
When subscribing to a channel we have to specify the whole path
Or use a wildcard
  +
  #

## Slide 31: Wildcards

## Slide 32: Chat with MQTT
chat.html

## Slide 33: MQTT Light Switch
lightSwitch.html
Use MQTT to send a message to the device to toggle an LED
  Format as JSON string
    {id:”YourID”, state:true/false}
  Your ID is the day of your birthday plus by 0 (male) or 32 (female)
  John was born on the 27th February, his ID is 27.
  Elizabeth was born on 11th May, her ID is 43
Add your code to ledMatrix.html to send the message

## Slide 34: Plotting Ambient Sensor Data
Add your code to sensorData.html
Receive sensor data via MQTT
  Format as a JSON string:
    {date, lightLevel:data, soundLevel:data}
Plot the data live with google charts